Flight Controls

Flight Control System Summary

- Moves and controls the aircraft during takeoff, flight, and landing

- Consists of cockpit controls, cables, pulleys, linkages, and bellcranks connected to the moveable control surfaces outside the airplane

- Primary Flight Controls

  - Ailerons

    - Controls longitudinal axis (bank)

  - Horizontal Stabilizer

    - Controls lateral axis (pitch)

  - Rudder

    - Controls vertical axis (yaw)

- Secondary Flight Controls

  - Flaps

    - Allows aircraft to be flown at a slower airspeed by increasing camber, thus increasing both lift and drag

    - Spring loaded to retract

    - Actuated by cables linked to the flap handle

    - Will not support weight while extended

  - Trim Controls

    - Pitch Trim

      - Anti-servo tab

      - Increase or decreases lift on the horizontal stabilizer

      - Always moves in the same direction

      - Enables pilot to trim out control pressure

    - Rudder Trim

      - Spring loaded centering device

      - Allows pilot to counter any prolonged yawing effects